## Slide 1: Introduction to Computer Science
William Hsu
Advanced Computation Laboratory
Department of Computer Science and Engineering
Department of Environmental Biology and Fisheries Science
National Taiwan Ocean University

## Slide 2: Chapter 4: Networking and the Internet
No one owns the Internet, and only one organization controls the Internet in its entirety. More of a concept than an actual tangible entity, the Internet relies on a physical infrastructure that connects networks to other networks. There are, however, organizations that oversee and standardize what happens on the Internet and assign IP addresses and domain names, such as the National Science Foundation, the Internet Engineering Task Force, ICANN, InterNIC and the Internet Architecture Board.

## Slide 3
4.1 Network Fundamentals
4.2 The Internet
4.3 The World Wide Web
4.4 Internet Protocols
4.5 Security

## Slide 4: Network Classifications
Scope
  Personal Area Network (PAN)
  Local Area Network (LAN)
  Campus Area Network (CAN)
  Metropolitan Area Network (MAN)
  Wide Area Network (WAN)
  Storage-Area Network (SAN)
  Virtual Private Network (VPN)
  Client Server Network
  Peer to Peer Network (P2P)
Ownership
  Closed versus open
Topology (configuration)
  Bus (Ethernet)
  Star (Wireless networks with central Access Point)
  Ring
  Tree (Hierarchical)
  Mesh

## Slide 5: Personal Area Network
Personal Area Network (PAN) is a computer network used for data transmission amongst devices such as computers, telephones, tablets and personal digital assistants.
Also Known as HAN (Home Area Network)
PANs can be used for communication amongst the personal devices themselves (interpersonal communication), or for connecting to a higher level network and the Internet (an uplink) where one "master" device takes up the role as internet router.

## Slide 6: Local Area Network
Xerox Corporation worked in collaboration with DEC and Intel to create Ethernet, which is the most pervasive LAN architecture used today.
Ethernet has evolved and has seen significant improvements in regard to speed and efficiency.
An upside of a LAN is fast data transfer with data speed that can reach up to 10Gbps.
Other significant LAN technologies are Fiber Distributed Data Interface (FDDI) and token ring.

## Slide 7: Campus Area Network
Larger than LANs, but smaller than metropolitan area networks these types of networks are typically seen in universities, large K-12 school districts or small businesses.
They can be spread across several buildings that are fairly close to each other so users can share resources

## Slide 8: Metropolitan Area Network
A MAN is larger than a LAN but smaller than or equal in size to a WAN.
The size range anywhere from 5 to 50km in diameter.
MANs are typically owned and managed by a single entity.
This could be an ISP or telecommunications company that sells its services to end-users in that metropolitan area.
For all intents and purposes, a MAN has the same characteristics as a WAN with distance constraints.

## Slide 9: Wide Area Network
A Wide Area Network exist over a large area
Data travels through telephone or cable lines
Usually requires a Modem
The world’s largest Wide Area Network in the Internet

## Slide 10: Storage Area Network
SAN may be referred to as a Sub network or special purpose network.
Its special purpose is to allow users on a larger network to connect various data storage devices with clusters of data servers.
SANs can be accessed in the same fashion as a drive attached to a server.

## Slide 11: Virtual Private Network
VPN is a private network that can access public networks remotely. VPN uses encryption and security protocols to retain privacy while it accesses outside resources.
When employed on a network, VPN enables an end user to create a virtual tunnel to a remote location. Typically, telecommuters use VPN to log in to their company networks from home.
Authentication is provided to validate the identities of the two peers.
Confidentiality provides encryption of the data to keep it private from prying eyes.
Integrity is used to ensure that the data sent between the two devices or sites has not been tampered with.

## Slide 12: Client/Server Network
In a client/server arrangement, network services are located on a dedicated computer called a server.
The server responds to the requests of clients.
The server is a central computer that is continuously available to respond to requests from clients for file, print, application, and other services.
Most network operating systems adopt the form of a client/server relationship.
Typically, desktop computers function as clients, and one or more computers with additional processing power, memory, and specialized software function as servers.

## Slide 13: Peer to Peer Network
Usually very small networks
Each workstation has equivalent capabilities and responsibilities
Does not require a switch or a hub.
These types of networks do not perform well under heavy data loads.

## Slide 14: Network Topologies
Network topology defines the structure of the network.
Physical topology:- It define the actual layout of the wire or media.
  Bus
  Ring
  Star
  Tree(Hierarchical)
  Mesh
Logical topology:- It defines how the hosts access the media to send data.
  Broadcast
  Token passing
Hybrid Topology

## Slide 15: Bus Topology
All devices are connected to a central cable, called bus or backbone.
There are terminators at each end of the bus that stops the signal and keeps it from traveling backwards.
T
T

## Slide 16: Communication Over a Bus Network

## Slide 17: Bus Topology
Advantages:
  There is no central controller.
  Control resides in each station
  The less interconnecting wire is required.
  Ease of installation.
  Backbone cable can be laid along the most efficient path, and then connected to the nodes by drop lines of various lengths
Disadvantages:
  It is possible that more than one station may attempt transmission simultaneously (collision or contention).
  Difficult reconfiguration and fault isolation.
  A fault or break in the bus cable stops all transmission, even between devices on the same side of the problem.
  The damaged area reflects signals in the direction of origin, creating noise in both directions

## Slide 18: Ring Topology
All devices are connected to one another in the shape of a closed loop.
Each device is connected directly to two other devices, one on either side of it.
Advantages:
  Avoids the collisions that are possible in the bus topology.
  Each pair of stations has a point-to-point connection.
  A signal is passed along the ring in one direction, from device to another, until it reaches its destination.
  Each device incorporates a repeater.
  Relatively easy to install and reconfigure.
  Fault isolation is simplified.
Disadvantages:
  A break in the ring (such as station disabled) can disable the entire network.
  Unidirectional traffic.

## Slide 19: Star Topology
All devices are connected to a central hub.
Nodes communicate across the network by passing data through the hub or switch.
Advantages:
  Easy to install and reconfigure.
  Robustness, if one link fails; only that link is affected. All other links remain active.
  Easy fault identification and isolation. As long as the hub is working, it can be used to monitor link problems and bypass defective links.
Disadvantages:
  The devices are not linked to each other.
  If one device wants to send data to another, it sends it to the controller, which then relays the data to the other connected device.

## Slide 20: Network Topologies (continued)

## Slide 21: Tree/Hierarchical Topology
Advantages:
  It allows more devices to be attached to a single central hub and can therefore increase the distance a signal can travel between devices.
  It allows the network to isolate and prioritize communications from different computers.
Disadvantages:
  The devices are not linked to each other.
  If one device wants to send data to another, it sends it to the controller, which then relays the data to the other connected device.
  The addition of secondary hubs brings two further advantages.

## Slide 22: Building a Large Bus Network from Smaller Ones

## Slide 23: Mesh Topology
Each host has its connections to all other hosts.
Mesh topology is implemented to provide as much protection as possible from interruption of service.
A nuclear power plant might use a mesh topology in the networked control systems.
Although the Internet has multiple paths to any one location, it does not adopt the full mesh topology.

## Slide 24: Mesh Topology
Advantages:
  The use of dedicated links guarantees that each connection can carry its data load, thus eliminating the traffic problems that can occur when links must be shared by multiple devices.
  It is robust, if one link becomes unusable, it does not incapacitate (affect) the entire system.
  Privacy and Security (every message sent travels along a dedicated line; only the intended recipient sees it).
  Point-to-point links make fault identification and fault isolation easy.
Disadvantages:
  A large amount of cabling required.
  A large amount of I/O ports required.
  Installation and reconfiguration are difficult.
  The sheer bulk of the wiring can be greater than the available space (in the walls, ceiling, or floors) can accommodate.
  The hardware required to connect each link (I/O ports and cables) can be prohibitively expensive.

## Slide 25: Wireless Networks
Wireless network is a type of computer network that uses wireless data connections for connecting network nodes.
Example
  Bluetooth
  Wi-Fi
  3G/4G

## Slide 26: Bluetooth
Bluetooth is a short-range wireless technology standard used for exchanging data between fixed and mobile devices over short distances.
It is using UHF radio waves in the ISM bands, from 2.402 GHz to 2.48 GHz.
The IEEE standardized Bluetooth as IEEE 802.15.1, but no longer maintains the standard.

## Slide 27: Wi-Fi
Wi-Fi Stands for Wireless Fidelity.
Wi-Fi, is a Local Area Wireless technology.
Wi-Fi networks use radio technologies to transmit and receive data at high speed.
It is based on the IEEE 802.11 family of standards.
Access point: The access point is a wireless LAN transceiver or “ base station” that can connect one or many wireless devices simultaneously to the internet

## Slide 28: Protocols
Rules by which activities are conducted on a network
  Example: Coordinating the transmission of messages between computers
    Need to avoid all machines transmitting at the same time
Allows vendors to build products that are compatible with products from other vendors

## Slide 29: Protocols
CSMA/CD
  Used in Ethernet
  Silent bus provides right to introduce new message
  Both machines stop and wait for a independent, random time
CSMA/CA
  Used in WiFi
  Hidden terminal problem
  Give advantage to the machine that has already been waiting

## Slide 30: The Hidden Terminal Problem

## Slide 31: Connecting Networks
Repeater: Extends a network.
  POE: Power over Ethernet.
Bridge: Connects two compatible networks.
  Bridges forward packets without analyzing and rerouting messages.
Switch: Connects several compatible networks.
  Hubs.
Router: Connects two incompatible networks resulting in a network of networks called an internet.
Power consumption and capability:
  Hubs < Bridges < Switches < Routers

## Slide 32: Network Interface Card
NIC is used to physically connect host devices to the network media.
A NIC is a printed circuit board that fits into the expansion slot of a bus on a computer motherboard.
NICs are sometimes called network adapters.
Each NIC is identified by a unique code called a Media Access Control (MAC) address.
This address is used to control data communication for the host on the network.

## Slide 33: Repeaters
A repeater is a network device used to regenerate a signal.
Repeaters regenerate analog or digital signals that are distorted by transmission loss due to attenuation.
A repeater does not make an intelligent decision concerning forwarding packets.

## Slide 34: Repeaters

## Slide 35: Hubs
A hub interconnects two or more workstations into a local area network.
  Allow the network to see them as a single unit.
When a workstation transmits to a hub, the hub immediately resends the data frame to all connecting links.
Active hubs concentrate hosts and also regenerate signals.
Hubs expand one Ethernet connection into many.
  For example, a four-port hub connects up to four machines.

## Slide 36: Bridge
A bridge connects networks and forwards frames from one network to another.
  If A sends a frame to E - the frame must be forwarded by the bridge.
  If A sends a frame to B - there is no reason to forward the frame.

## Slide 37: Bridges
Bridges convert network data formats and perform basic data transmission management.
Bridges provide connections between LANs.
They also check data to determine if it should cross the bridge. This makes each part of the network more efficient

## Slide 38: Switches
A switch is a combination of a hub and a bridge.
It can interconnect two or more workstations, but like a bridge, it observes traffic flow and learns.
When a frame arrives at a switch, the switch examines the destination address and forwards the frame out the one necessary connection.
The backplane of a switch is fast enough to support multiple data transfers at one time.
  Multiple workstations connected to a switch use dedicated segments.
  This is a very efficient way to isolate heavy users from the network.

## Slide 39: Routers
Routers have all the capabilities listed above.
Routers can regenerate signals, concentrate multiple connections, convert data transmission formats, and manage data transfers.
They can also connect to a WAN, which allows them to connect LANs that are separated by great distances.

## Slide 40: Routers
Specialized computers.
The device that connects a LAN to a WAN or a WAN to a WAN (the INTERNET! – uses IP addresses).
A router accepts an outgoing packet, removes any LAN headers and trailers, and encapsulates the necessary WAN headers and trailers.
  Because a router has to make wide area network routing decisions, the router has to dig down into the network layer of the packet to retrieve the network destination address.
Thus, routers are often called “layer 3 devices”.
  They operate at the third layer, or OSI network layer, of the packet.

## Slide 41: Routers Connecting Two WiFi Networks and an Ethernet Network to Form an Internet

## Slide 42: Gateway
A gateway is a piece of networking hardware used in telecommunications for telecommunications networks that allows data to flow from one discrete network to another.
Gateways are distinct from routers or switches in that they communicate using more than one protocol to connect a bunch of networks

## Slide 43: Firewall
A firewall is a network device or software for controlling network security and access rules.
Firewalls are inserted in connections between secure internal networks and potentially insecure external networks such as the Internet.
Firewalls are typically configured to reject access requests from unrecognized sources while allowing actions from recognized ones.
The vital role firewalls play in network security grows in parallel with the constant increase in cyber attacks.

## Slide 44: Network Media
The function of the media is to carry a flow of information through a LAN.
Wired Media:- A widely adopted family that uses copper and fiber media in local area network (LAN) technology are collectively known as Ethernet
  Copper Cable
  Coaxial Cables
  Shielded Twisted Pair(STP)
  Unshielded Twisted Pair
Fibre Optic Cable
Wireless Media:- use the atmosphere, or space, as the medium.

## Slide 45: Copper Cable
The most common, easiest, quickest, and cheapest form of network media to install.
The disadvantage of sending data over copper wire is that the further the signal travels, the weaker it becomes.

## Slide 46: Coaxial Cable
It can be run longer distances than Twisted pair Cables.
Speed: 10-100Mbps
  Cost: Inexpensive
  Media and connector size: Medium
  Maximum cable length: 500m

## Slide 47: Shielded Twisted Pair(STP)
Speed: 0-100Mbps
Cost: Moderate
Media and connector size: Medium to large
Maximum cable length: 100m

## Slide 48: Unshielded Twisted Pair
UTP is a four-pair wire medium used in a variety of networks.
Each of the eight copper wires in the UTP cable is covered by insulating material.
  Speed: 10-100-1000 Mbps*
  Cost: Least Expensive
  Media and connector size: Small
  Maximum cable length: 100m * (Depending on the quality/category of cable)

## Slide 49: UTP Implementation
EIA/TIA specifies an RJ-45 connector for UTP cable.
The letters RJ stand for registered jack.

## Slide 50: Inter-process Communication
Client-server
  One server, many clients.
  Server must execute continuously.
  Client initiates communication.
Peer-to-peer (P2P)
  Two processes communicating as equals.
  Peer processes can be short-lived.

## Slide 51: The Client/Server Model Compared to the Peer-to-Peer Model

## Slide 52: Distributed Systems
Systems with parts that run on different computers
  Cluster computing
    Cluster differs from Cloud and Grid in that a cluster is a group of computers connected by a local area network (LAN).
    Cluster is tightly coupled, whereas a Grid or a Cloud is loosely coupled.
    Clusters are made up of machines with similar hardware, whereas clouds and grids are made up of machines with possibly very different hardware configurations.
  Grid computing
    Millions of home PCs (not connected to each other) work on a complex problem
    Cloud and grid are more wide scale and can be geographically distributed.
      FutureGrid
  Cloud computing
    Provide services, hide the details
    Amazon’s Elastic Compute Cloud.
    Google Drive, Gmail, Facebook, Youtube, Dropbox…

## Slide 53: Cloud Computing
Cloud computing is Internet-based computing, whereby shared resources, software, and information are provided to computers and other devices on demand, like the electricity grid.
A Cloud is a type of parallel and distributed system consisting of a collection of interconnected and virtualized computers that are dynamically provisioned and presented as one or more unified computing resources based on service-level agreements established through negotiation between the service provider and consumers.

## Slide 54: Properties & Characteristics

## Slide 55: IaaS
Infrastructure as a Service – IaaS
  The capability provided to the consumer is to provision processing, storage, networks, and other fundamental computing resources where the consumer is able to deploy and run arbitrary software, which can include operating systems and applications.
  The consumer does not manage or control the underlying cloud infrastructure but has control over operating systems, storage, deployed applications, and possibly limited control of select networking components .
Examples :
  Amazon EC2
  Eucalyputs
  OpenNebula

## Slide 56: PaaS
Platform as a Service – PaaS
  The capability provided to the consumer is to deploy onto the cloud infrastructure consumer-created or acquired applications created using programming languages and tools supported by the provider.
  The consumer does not manage or control the underlying cloud infrastructure including network, servers, operating systems, or storage, but has control over the deployed applications and possibly application hosting environment configurations.
Examples :
  Microsoft Windows Azure
  Google App Engine
  Hadoop(High Availability Distributed Object Oriented Platform)

## Slide 57: SaaS
Software as a Service – SaaS
  The capability provided to the consumer is to use the provider’s applications running on a cloud infrastructure. The applications are accessible from various client devices through a thin client interface such as a web browser (e.g., web-based email).
  The consumer does not manage or control the underlying cloud infrastructure including network, servers, operating systems, storage, or even individual application capabilities, with the possible exception of limited user-specific application configuration settings.
Examples :
  Google Apps (e.g., Gmail, Google Docs, Google sites, …etc)

## Slide 58: The Internet
The Internet: An internet that spans the world.
  Original goal was to develop a means of connecting networks that would not be disrupted by local disasters.
  Today a commercial undertaking that links a worldwide combination of PANs, LANs, MANs, and WANs involving millions of computers.

## Slide 59: How Information Travel Through the Internet
When you connect to a Web site through an ISP and start exchanging information, there isn't a fixed connection between your computer and the Web server computer hosting the Web site.
Information is exchanged using the best possible path at that particular time.
Special computers called routers determine these paths, avoiding slow links and favoring fast ones.
Your Computer
ISP
Routers
Web Servers

## Slide 60: Internet Architecture
Internet Service Provider (ISP)
  Tier-1: ISP that has access to the entire Internet Region solely via its free and reciprocal peering agreements.
  Tier-2: A Tier 2 ISP is an Internet Service Provider that purchases transit to reach some destination(s) within an Internet Region.
Access or tier-3 ISP: A network that solely purchases transit from other networks to reach the Internet.
  Provides connectivity to the Internet.
  Hot spot (wireless)
  Telephone lines
  Cable/Satellite systems DSL
  Fiber optics

## Slide 61: Internet Composition

## Slide 62: Internet Addressing
IP address: pattern of 32 or 128 bits often represented in dotted decimal notation
  IPv4
  IPv6
Mnemonic address:
  Domain names
  Top-Level Domains
    .org, .gov, .com, .mil, .net, .au, .ca, .biz, ….
Domain name system (DNS)
  Name servers
  DNS lookup

## Slide 63: Internet Corporation for Assigned Names & Numbers (ICANN)
Allocates IP addresses to ISPs who then assign those addresses within their regions.
Oversees the registration of domains and domain names.

## Slide 64: IP addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one interface
  IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 65: Subnets
IP address:
  subnet part - high order bits
  host part - low order bits
What’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 66: Subnets
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 67: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 68: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 69: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 70: DHCP: Dynamic Host Configuration Protocol
Goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 71: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 72: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs

## Slide 73: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 74: Domain name system
A system that can map a name to an address or an address to a name.
DNS is a protocol that can be used in different platforms.

## Slide 75: Domain name system
Domain Name System
Distributed database
  No centralization
Simple client/server architecture
  UDP port 53, some implementations also use TCP
Hierarchical namespace
  As opposed to original, flat namespace
  e.g. .com  google.com  mail.google.com

## Slide 76: Domain name system
Contacted by local name server that can not resolve name
Root name server:
  Knows the authoritative name server for main domain
~ 60 root name servers worldwide
  Real-world application of anycast

## Slide 77: Domain name system

## Slide 78: Domain name system

## Slide 79: Domain name system

## Slide 80: Domain name system

## Slide 81: Resolving DNS - Iterative

## Slide 82: Resolving DNS - Recursive

## Slide 83: Early Internet Applications
Network News Transfer Protocol (NNTP)
File Transfer Protocol (FTP)
Telnet and SSH
Hypertext Transfer Protocol (HTTP)
Electronic Mail (email)
  Domain mail server collects incoming mail and transmits outing mail.
  Mail server delivers collected incoming mail to clients via POP3 or IMAP.

## Slide 84: SMTP Simple Mail Transfer Protocol
220 mail.tardis.edu SMTP Sendmail Gallifrey-1.0; Fri, 23 Aug 2413 14:34:10
HELO mail.skaro.gov
250 mail.tardis.edu Hello mail.skaro.gov, pleased to meet you
MAIL From: dalek@skaro.gov
250 2.1.0 dalek@skaro.gov... Sender ok
RCPT To: doctor@tardis.edu
250 2.1.5 doctor@tardis.edu... Recipient ok
DATA
354 Enter mail, end with "." on a line by itself
Subject: Extermination.
EXTERMINATE!
Regards, Dalek
.
250 2.0.0 r7NJYAEl028071 Message accepted for delivery
QUIT
221 2.0.0 mail.tardis.edu closing connection

## Slide 85: More Recent Applications
Voice Over IP (VoIP)
Internet Multimedia Streaming
  N-unicast
  Multicast
  On-demand streaming
  Content delivery networks (CDNs)

## Slide 86: World Wide Web
Hypertext combines internet technology with concept of linked-documents.
  Embeds hyperlinks to other documents.
Browsers present materials to the user.
Webservers provide access to documents.
Documents are identified by URLs and transferred using HTTP.
  URL: Uniform Resource Locator
  URI: Uniform Resource Indentifier
  A URI is an identifier for some resource, but a URL gives you specific information as to obtain that resource.

## Slide 87: A Typical URL

## Slide 88: Hypertext Markup Language (HTML)
Encoded as text file
Contains tags to communicate with browser
  Appearance
    <h1> to start a level one heading
    <p> to start a new paragraph
  Links to other documents and content
    <a href = . . . >
  Insert images
    <img src = . . . >

## Slide 89: A Simple Webpage

## Slide 90: A Simple Webpage (continued)

## Slide 91: An Enhanced Simple Webpage

## Slide 92: An Enhanced Simple Web Page (continued)

## Slide 93: Extensible Markup Language (XML)
XML: A language for constructing markup languages similar to HTML
  A descendant of SGML
  Opens door to a World Wide Semantic Web

## Slide 94: Using XML
<staff clef = “treble”> <key>C minor</key>
<time> 2/4 </time>
<measure> < rest> egth </rest> <notes> egth G, egth G, egth G </notes></measure>
<measure> <notes> hlf E </notes></measure>
</staff>

## Slide 95: The First Two Bars of Beethoven’s Fifth Symphony

## Slide 96: MathMLs
Mathematical Markup Language (MathML): Special form of markup language.

## Slide 97: Client Side vs Server Side
Client-side activities
  Javascript
  Macromedia Flash
Server-side activities
  Common Gateway Interface (CGI)
  Servlets
  JavaServer Pages (JSP) / Active Server Pages (ASP)
  PHP
  Python, Perl

## Slide 98: Internet Protocols
Control how messages are transferred over the Internet
This software must reside on every computer in the Internet
Accomplished by a multi-level hierarchy

## Slide 99: Package-shipping Example

## Slide 100: Internet packet encapsulation

## Slide 101: Internet Software Layers
Application: Constructs message with address.
Transport: Chops message into packets.
Network: Handles routing through the Internet.
Link: Handles actual transmission of packets.

## Slide 102: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 103: IP fragmentation, reassembly
Network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
Large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 104: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 105: TCP vs UDP Packet

## Slide 106: Following a message through the Internet

## Slide 107: TCP/IP Protocol Suite
Transport Layer
  Transmission Control Protocol (TCP)
  User Datagram Protocol (UDP)
Network Layer
  Internet Protocol (IP)
    IPv4
    IPv6

## Slide 108: TCP/IP Stack
A protocol stack is a group of protocols that all work together to allow software or hardware to perform a function.
The TCP/IP protocol stack is a good example.
It uses four layers that map to the OSI model.

## Slide 109: TCP/IP Stack
Layer 1: Network Interface - This layer combines the Physical and Data layers and routes the data between devices on the same network. It also manages the exchange of data between the network and other devices.
Layer 2: Internet - This layer corresponds to the Network layer. The Internet Protocol (IP) uses the IP address, consisting of a Network Identifier and a Host Identifier, to determine the address of the device it is communicating with.

## Slide 110: TCP/IP Stack
Layer 3: Transport - Corresponding to the OSI Transport layer, this is the part of the protocol stack where the Transport Control Protocol (TCP) can be found.
  TCP works by asking another device on the network if it is willing to accept information from the local device.
Layer 4: Application - Layer 4 combines the Session, Presentation and Application layers of the OSI model.
  Protocols for specific functions such as e-mail (Simple Mail Transfer Protocol, SMTP) and file transfer (File Transfer Protocol, FTP) reside at this level.

## Slide 111: Choosing between TCP and UDP

## Slide 112: Multiplexing Datagrams

## Slide 114: RJ-45

## Slide 115: Cybersecurity
Attacks
  Malware (viruses, worms, Trojan horses, spyware, phishing software)
  Denial of service (DoS)
  Spam
Protection
  Firewalls
  Spam filters
  Proxy Servers
  Antivirus software

## Slide 116: Encryption
HTTPS and SSL
Public-key Encryption
  Public key: Used to encrypt messages
  Private key: Used to decrypt messages
Certificates and Digital Signatures
  Certificate authorities

## Slide 117: Public-key Encryption

## Slide 118: Legal approaches to network security
Computer Fraud and Abuse Act
Electronic Communication Privacy Act
USA PATRIOT Act
Communications Assistance for Law Enforcement Act
Anticybersquatting Consumer Protection Act

## Slide 119: Security vs Privacy
Security: Can you keep things out of reach from others.
Privacy: Can you keep your things to yourself.